## Slide 1: Chemical Hazard
Notes: <number>

## Slide 2: Then……and……Now
Notes: <number>

## Slide 3: What will we learn today?
Method to identify and control workplace hazards
Common laboratory hazards
Control measures
Notes: <number>

## Slide 4: Laboratory Safety
Anticipation
Recognition
Evaluation
Control
Notes: <number>

## Slide 5: Laboratory Safety
Anticipation
  Evaluate the process before getting started
  List or identify potential hazards
Anticipation
Notes: <number>

## Slide 6: Laboratory Safety
Recognition
  For ongoing or existing operation
  List or identify potential hazards
  Hazardous material
Recognition
Notes: <number>

## Slide 7: Types of Hazardous Materials
Flammable/Combustible
Corrosive
Oxidizer
Toxic
Water Reactive
Recognition
Notes: <number>

## Slide 8: Flammable/Combustible
Recognition
Notes: <number>
Liquid
  Flashpoint below 200oF
Gas
  At ambient temp. and pres. forms a range of flammable mixtures wider than 12% by volume regardless of LEL
Solid
  Liable to cause fire through friction, absorption of moisture, spontaneous chemical change, or which can be ignited readily burning at a rate of greater than 1/10 in. per second.

## Slide 9: Flammable (OSHA)
Liquid
  Flashpoint below 200oF is combustible
Gas
  Explosive range greater than 12%
Solid
  fire through friction, absorption of moisture, spontaneous chemical change, or readily burns at greater than 1/10 in. per second.
Recognition
Notes: <number>

## Slide 10: Corrosive
Recognition
Notes: <number>
pH >12.5 or <2
A chemical that causes visible destruction of, or irreversible alterations in, living tissue by chemical action at the point of contact. This term does not refer to action on inanimate surfaces.
Any material that will corrode steel at a rate of 0.25 in. per year

## Slide 11: Corrosive
pH >12.5 or <2
Any material that will corrode steel at a rate of 0.25 in. per year
Causes visible destruction of living tissue
Recognition
Notes: <number>

## Slide 12: Oxidizers
Recognition
Notes: <number>

## Slide 13: Oxidizer
A chemical that initiates or promotes combustion in other materials
A material that may, generally by yielding oxygen, cause or enhance the combustion of other materials
May lower the ignition temperature and flashpoint
Recognition
Notes: <number>

## Slide 14: Toxic Materials
Recognition
Notes: <number>

## Slide 15: Toxic Materials
LD50 below 500 mg/kg
Acute toxics below 50 mg/kg
Recognition
Notes: <number>

## Slide 16: Water Reactive
Recognition
Notes: <number>
A chemical that reacts with water to release gas that is either flammable or presents a health hazard
(Potassium metal)

## Slide 17: Water Reactive
A chemical that reacts with water to release gas that is either flammable or presents a health hazard
Recognition
Notes: <number>

## Slide 18: Hazard Evaluation
Evaluation -- Chemical hazards
    MSDS
    NFPA
    Manufacturer label
    TLV/PEL
    NIOSH pocket guide
Evaluation
Notes: <number>

## Slide 19: Hazard Evaluation
Read the bottle labels
Evaluation
Notes: <number>

## Slide 20: NFPA Diamond
4 sections colored blue, red, yellow and white
Hazards are rated on a scale of 5, 4 being highest
Colored diamonds
Meant for fire fighters and emergency responders
White area used for special hazards
Evaluation
Notes: <number>

## Slide 21: Common Symbols
ACID This indicates that the material is an acid, a corrosive material that has a pH lower than 7.0
ALK This denotes an alkaline material, also called a base. These caustic materials have a pH greater than 7.0
COR This denotes a material that is corrosive (it could be either an acid or a base).
This is a another symbol used for corrosive.
The skull and crossbones is used to denote a poison or highly toxic material.
Radioactive hazards
Indicates an explosive material.
Evaluation
Notes: <number>

## Slide 22: Hazard Evaluation
Read the MSDS for the chemical
Evaluation
Notes: <number>

## Slide 23: Hazard Evaluation
Contact the Health and Safety officer
Evaluation
Notes: <number>

## Slide 24: Hazard Evaluation
Contact the manufacturer
Evaluation
Notes: <number>

## Slide 25: Ventilation
Chemical fume hoods
Control
Notes: <number>

## Slide 26: Ventilation
Control
Notes: <number>

## Slide 27: Ventilation
Snorkels
Control
Notes: <number>

## Slide 28: Signs
Control
Notes: <number>

## Slide 29: Signs
Control
Notes: <number>

## Slide 30: Exposure Control Plan
Exposure determination
Communications of hazards
Record keeping
Control
Notes: <number>

## Slide 31: Chemical Hygiene Plan
Basic rules and procedures
Chemical handling
Environmental monitoring
Housekeeping
Medical program
PPE
Records
Signs and labels
Spills
Training
Waste
Control
Notes: <number>

## Slide 32: Personal Protective Equipment
Gloves
Safety glasses
Lab coats
Respirators
Control
Notes: <number>

## Slide 33: PPE
Control
Notes: <number>

## Slide 34: QUESTIONS?
Notes: <number>