## Slide 1: Introduction
Relationship between power,
current, voltage and resistance:
P = power (watts)
I = current (amperes)
V = voltage (volts)
R = resistance (ohms)
Example:
Heating tape uses 5 amps at 120 volts.
Power dissipated by this device is 600 watts.
Notes: <number>

## Slide 2: AC vs. DC Electricity
Direct current (DC)
Alternating current (AC)
Notes: <number>

## Slide 3: Lab Equipment
Power requirements (input)
Equipment | Volts | Amps | Watts
PC | 120 | 6.0 | 720
Monitor | 120 | 1.5 | 180
Turbopump | 120 | 4.0 | 480
Cryopump | 240 | 12.0 | 2,880
Heating tape (big) | 120 | 6.92 | 830
Heat gun | 120 | 14.0 | 1680
Notes: <number>

## Slide 4: Lethal Electricity
Chart below assumes 1 second hand to foot
exposure to 120 volt, 60 cycle AC power supply.
Current | Reaction
1 mA | Perception
5 mA | Slight shock felt; not painful but disturbing
6-30 mA | Painful shock; "let-go" range
50-150 mA | Extreme pain, respiratory arrest, severe muscular contraction
1,000-4,300 mA | Ventricular fibrillation
10,000+ mA | Cardiac arrest, severe burns and probable death
Laboratory wall outlets provide 20,000 mA !!
Notes: <number>

## Slide 5: Safety Devices
Fuses
Protect electrical wiring from carrying too much current.
Protect malfunctioning equipment from drawing too much current.
Conductor melts if too much current flows through fuse.
Can only be used once.
Always use the correct fuse.
New fuse
Blown fuse
Notes: <number>

## Slide 6: Safety Devices
Circuit Breakers
Protect electrical wiring from carrying too much current.
Mechanical switch is driven by an electromagnet.
Can only be reset many times.
Notes: <number>

## Slide 7: Safety Devices
Circuit Breakers
One circuit breaker may cover many electrical receptacles in a lab.
Receptacles in some labs are labeled with a number that corresponds to a circuit breaker.
Notes: <number>

## Slide 8: Preventing Accidents
Avoid contact with energized circuits.
Disconnect the power source before servicing or repairing electrical equipment.
Work with only one hand, keeping the other hand behind you or in a pocket.
If water or a chemical is spilled onto equipment, shut off power at the main switch or circuit breaker and unplug the equipment.
If an individual comes in contact with a live electrical conductor, do not touch the equipment, cord or person.
Disconnect the power source from the circuit breaker or pull out the plug using a leather belt .
Notes: <number>

## Slide 9: Preventing Accidents
Electrical Fires
Unplug equipment first.
Use dry chemical fire extinguisher.
If fire is large, unplug equipment and call fire dept.
Never use water!!
Notes: <number>

## Slide 10: Conclusions
Be careful with electricity.
Ask someone for help if you are unsure.
Notes: <number>

## Slide 11: Electricity
Recognition
Notes: <number>

## Slide 12: Electricity
Recognition
Notes: <number>